Guangzhou jurong electro co.,ltd  Vehicle LCD Monitor

JL JL2415  Installment Diagram 2

JL2415 Installment Diagram 3

Vehicle LCD Monitor

Vehicle LCD Monitor

III、Operation

1、After opening the signal source and the switch power, it costs about 5 seconds to have the clear image of the programmer.

2、To set the specifications of the image (Generally, it is not necessary to adjust the specifications as it has been set to the best mode when was delivered from the factory)

- MENU:  OSD OFF to active the menu；OSD On to active the submenu 。

- +/-： OSD ON turn down/up the volume

IV、Specification

Name ： Vehicle LCD Monitor

Item Number：JL2415GB JL1415GT

TV Mode： PAL / NTSC

Driver Element： a-Si  TFT  LCD

Screen Diagonal： 15inches 304.1(H)×228.1(V)  17inches 337.92(H)×270.34(V)

Pixel Number： 15inches 1024（H）×768（V） 17inches 1280（H）×1024（V）

Brightness： 15inches 250 cd/m2   17inches300/400 cd/m2

Contrast Ratio： 15inches 500∶1 17inches 500∶1

Response Time： ≤12ms

Viewing Angle： ≥65º/65º（Left/Right），≥65º/55º（Up/Down）

Connector： 1、CVBS video input connector

2、+24Vpower input connector

Power： +24V DC

Power： 40W (MAX)

Weight： 15inches Fixed  5kg       15inches Manual Flip  6.5kg

17inches Fixed  6.5kg     17inches Manual Flip  8kg

Environment:

Temperature：   0℃～50℃

Contract Wet：  10%～90%

Press：        86KPa～106Kpa

Vehicle LCD Monitor

II、Installation

Installation is simple. Please refer to the diagram following:

JL2415 Installment Diagram 1

JURONG

Vehicle LCD Monitor

Contents

I、Precaution     ············································  1

II、Installation    ············································  2

III、Operation     ············································  3

IV、Specification  ············································  3

V、Before Repair  ············································  4

VI、Package     ·············································  4

Thank you for purchasing Vehicle LCD Monitor of Changyu Electron. To ensure the best use of the unit, please read this handbook carefully beforehand. Please keep this handbook for using in the future.

This product has the features of high quality of display, lightweight, electricity saving and no radiation. You will be certainly benefit from this LCD for its comfort, safety and space saving. The outlook of this product is nice and anti-pound. The installation is not complicate and this product can be connected directly to the power of the vehicle.

I、Precaution

1、Do not take part the product and fix it by yourself. If there is some problem with it, please turn off the power first, and then inform our company or consignee. The system of the product is consisted of lots of accurate electronic components. If it is taken apart or changed, it will be probably destroyed.

2、Try to get rid of wet, dust, steam, soot and direct sunshine when you store and use this product.

a、Do not use chemical solutions to clean this product. Please simply wipe with a clean soft cloth.

b、Storage temperature:-20℃～60℃

Using temperature: 0℃～50℃

c、LCD is supply with the vehicle power of +24V (vehicle with the negative pole grounding and +24V power)

Note: For the safety, do not watch the programmer or operate this product when driving

Vehicle LCD Monitor

V、Before Repair

Please check in the below ways before repair.

| Problem | Cause & Possible Solution |
| --- | --- |
| No Picture | Whether Signal resource is normal Please turn off the power and turn on after 5 seconds Whether CVBS signal wire and plug connected well |
| No Sound | ◇ No sound system in the unit. Please use the sound system of the vehicle |
| Image | Check the environment temperature Check direct strong sunshine ◇ check the “Brightness” and “Contrast Ratio” |
| Interference | ◇ Check there is no interference from Car Motor, Car Electron, High Voltage Wire and neon light |
| No Color | ◇Weakness of the signal |

Note：When no signal, there will be “No signal” appearing on the screen then comes the dark screen.

VI、Package

Supplied Components:

LCD Monitor                  Q’ty: 1

Installation Accessories          Q’ty: 1

Material: Instructions, Warranty Card

Note: Accessories and their parts numbers are subject to modification without prior notice due to improvements.

JURONG

NO.2Dongsheng road,Huaxing industrial Zone,Xinhua Street,Huadu District,Guangzhou City,Guangdong,ChinaService Hotline：86-20-28608483 Tel：86-13725447670 Fax：86-20-36826586 P.C：510800

# Text boxes

. 1 .

. 6 .

. 4 .

. 3 .

Vehicle LCD Monitor

## FIXED OR MANUAL FLIP

Guangzhou jurong electron Co.,Ltd

Shenzhen Changyu Electron Co.,Ltd

JL2515 Installment Diagram 4

Operating Instructions

. 5 .

. 2 .